## Slide 1: REP TRAINING
Controls

## Slide 2: What We Will Cover

## Slide 3: What We Will Cover
Scope
Control Alarms and Modes
Control Methodologies
Control hardware from OEMCtrl (LS-1628u / Equipment Touch v3 / ZSensor)
Sequences of Operations (SOO)

## Slide 4: Scope Purpose of Controls
Protect Equipment
Communicate Status (BAS/HMI)
Operational Efficiency
Notes: Our controls act in a three fold manner. First, is to protect the equipment from damage to itself or from damaging property. Next, is to make available pertinent data and alarms to the people operating the equipment, via touchscreen, PC or BAS frontend. Ultimately, with these fundamentals handled, the control logic enables intelligent use of kWh to deliver the most efficient conditioning of supply air.

## Slide 5: Topic Indicators
Notes: The rest of what we talk about falls under at least one of these three categories, sometimes more!

## Slide 6: Available Alarms
  Alarm Definitions
    Life safety (ie. Smoke Detection, High CO2)
    Critical Lockout (High Pressure, etc)
    Urgent “Trip” (1st and 2nd alarms of HPS, LPS, etc)
    Normal message
  Alarm Information Provided:
    Timestamp, Alarm Name, Critical (Y/N), Lockout (Y/N)
  Generally, “three strikes you’re out”
Notes: The rest of what we talk about falls under one of these three categories

## Slide 7: Available Alarms
Alarms
T.24 FDD
SF Hand/Stp
ExFan Hand/Stop
HPS Hand/Stop
DX Freeze
Heat Fail
Water Flow Switch
Smoke
Sensor Fail
Comp Hand/Stop
LPS Hand/Stop
High/Lo SAT
Water Freeze
Dirty Filter
Cond Ovrflw
High CO2
Notes: The rest of what we talk about falls under one of these three categories

## Slide 8: Communications - BACnet
Our controller is BTL Certified which guarantees interoperability with all major BAS frontends and devices.
BACnet IP
BACnet MS/TP
Notes: The rest of what we talk about falls under at least one of these three categories, sometimes more!

## Slide 9: Communications - BACnet
  BACnet Point Properties
  AO - Analog Output
  BO - Binary Output
  AI - Analog Inputs
  BI - Binary Inputs
  AV – Analog Value
  BV – Binary Value
  Present Value
  Relinquish Default Value
  Priority Array
  Point Address (Object ID)
Notes: The rest of what we talk about falls under at least one of these three categories, sometimes more!

## Slide 10: Communications - BACnet
Notes: The rest of what we talk about falls under at least one of these three categories, sometimes more!

## Slide 11: Control Methodologies (PID Feedback)
Proportional
Integral
Derivative
Sensor
Setpoint
How FAR away from setpoint?
How LONG has it been away?
How FAST is it trending toward or away?
Notes: Provide uniform sequences of operating HVAC DOAS units to ensure maximum performance.
  Provide feedback loops for proper controls
  Sensors need to be placed in the correct locations
  PID Control loops need to utilize the input signals to meet the desired setpoints (Heating and Cooling Loops)
  Not all control loops need to be PID loops
  PID loops shall be capable of limiting the rate of change
  Adjustable set points with dead bands
  Trim and Respond set point logic for critical zone control

## Slide 12: Control Methodologies (PID Feedback)
Enabled
Setpoint
Sensor
Control Signal
PROCESS PID
Notes: The requirements for a PID to operate. Usually the “D” term is set to zero.

## Slide 13: Control Methodologies (PID Feedback)
Notes: Exaggerated example of PID control showing different tuned parameters for a step response (setpoint change, e.g.)

## Slide 14: Control Methodologies, Hot Gas Reheat Valve example
Notes: Example of Addison Standard program code controlling the HGRH valve enabled by dehumidification conditions and controlled by SAT Drybulb setpoint.

## Slide 15: Control Methodologies, Hot Gas Reheat Valve example
Enabled
Setpoint
Sensor
Control Signal
Notes: Example of Addison Standard program code controlling the HGRH valve enabled by dehumidification conditions and controlled by SAT Drybulb setpoint.

## Slide 16: Example of Control Modes
Notes: This is an abbreviated list of possible operating modes of our standard program. Based on the application and what has been enabled

## Slide 17: Enabling Technologies OPTICORE LS-1628u
32-bit ARM core, Linux kernel
16GB Flash memory, 512MB RAM
Universal Inputs and Outputs
Performance / Hardware
Communication Features:
3 Configurable Communication Ports
  Gig-E: Gigabit Ethernet Port for BACnet/IP or Modbus/TCP, also allows addressing via DHCP
  Port S1: Rotary configurable EIA-485 Port for BACnet MS/TP or Modbus
  Port S2: Firmware configurable EIA-485 Port for BACnet MS/TP or Modbus
6 Dedicated Communication Ports
  Service Port: 10/100 Ethernet port for technician access and touchscreen connection
  Rnet: ALC proprietary Sensor Network. Can be used for touchscreen connection
  I/O Bus Port: for I/O point expansion via screw terminal for remote mounting
  I/O Bus Edge Connector: for I/O point expansion (includes power)
  Act Net: Network of communicating valves and actuator
  Comm Expansion Edge Connector Port: for comm expansion

## Slide 18: OPTICORE LS-1628u

## Slide 19: Enabling Technologies OptiCore Equipment Touch 3 (EQT3)
Fanless cooling system and ultra-low power consumption
Front IP65 water and dust proof
Access to most data points in the controller
Support for graphics and animations
Schedule Interface – view and edit BACnet schedules
Alarm Viewing – view the controls alarm history buffer
Customize for any application
NEW! Can access Service Port Page for communications setup

## Slide 20: OPTICORE EQT3 Displays

## Slide 21: OPTICORE EQT3 Displays
Sample Screenshots

## Slide 22: OPTICORE EQT3 Displays
Sample Screenshots

## Slide 23: OPTICORE EQT3 Displays
Sample Screenshots

## Slide 24: Displays EQ-10,EQ-7,EQ-2

## Slide 25: Enabling Technologies: ZS Sensors
Provide flexibility for multiple building applications
Low-profile, neutral color scheme
Efficient options for multiple sensors in one case
Units are daisy chainable, can control on average or min/max
Discreet service port for laptops to access the LS-1628u
Mounts on a standard 2 inch by 4-inch electrical box
Combinations can include zone temperature and/or relative humidity, CO2, VOC
Multiple models offer a choice of options, including a large easy-to-read display, local setpoint adjustment, local override, and fan control

## Slide 26: ZS Sensors

## Slide 27: ZS Sensors

## Slide 28: Sequences of Operation
Addison’s Sequence of Operation is generated dynamically based on equipment code string
Standard set of control methods are written (enabled) to the control program at the end of the production line
Custom ‘special’ Sequences can be generated by Addison Controls Engineering, at cost

## Slide 29: One More Thing…
Notes: Enabling network and software technologies will be added to the LS-1628u in 2024, allowing for an even more feature rich offering and competitive capabilities!

## Slide 30: THANK YOU